## Slide 1: RCIM
Prepared by Yakima County Public Services

## Slide 2: CATEGORIES
Residential onsite Sewage Systems (ROSS)
Large Onsite Sewage Systems (LOSS)
Commercial Onsite Septic Systems (COSS)
Residential Lawn Fertilizers
Small Scale Commercial and Hobby Farms

## Slide 3: ROSS – Data
6,044 Households Utilize ROSS
Average Household Size Range = 2.72 to 4.16 persons per household (OFM 2010)
Approximate Location of each ROSS Determined – (GIS)
Soil Type at Approximate Location Determined – (NRCS 2014)
Land Elevation Determined – (GIS Land Elevation Model)
Approximate Depth to Groundwater Determined (USGS – Vaccaro el al. 2009)

## Slide 4: ROSS – Data Inputs
TN Loading to a ROSS Ranges from 6 to 17 grams per person per day (EPA 2002a and 1992)
  Low - 6 gm/cap/day
  Medium - 11.2 gm/cap/day
  High – 17 gm/cap/day
Denitrification - the conversion of nitrates into nitrogen gas which is then released into the atmosphere. This is caused by bacteria and is dependent upon environmental conditions existing in the soils below a drain field
  GWMA soils are predominately sands, silts, silty loams and clay loams (GIS and NRCS). These soils are favorable for denitrification (EPA 2002a)
    Denitrification requires Aerobic (unsaturated) soil conditions – The depth to groundwater at over 90% of GWMA ROSS locations is greater than 10 feet (GIS and Vaccaro et al. 2009).

## Slide 5: ROSS – Data Inputs (continued)
Denitrification (continued)
  Denitrification amounts are difficult to predict.
    Studies have shown that 10% to 40% of TN can be removed (EPA 2002a)
    Most common removal rates are between 10% and 20%
    Conservative Denitrification rates used in study:
      Low – 20%
      Medium 15%
      High 10%

## Slide 6: ROSS – Data Inputs (continued)
Septage Removal – the periodic pumping of septic tanks removes some TN from entering the drain field
  Average TN in septage is 588 mg/l (EPA 1994)
  Minimum tank size = 900 gallons (WAC 246-272A-0010)
  TN in tank when “full” = 4.4 pounds (2Kg)
  Recommended Pumping Frequency every 3 to 5 years
  82% responded to Well Assessment Survey that they have their tank pumped regularly
  Report uses conservative pumping frequency
    Low – every 3 years
    Medium – every 5 years
    High – every 10 years

## Slide 7: ROSS – Data Input Summary
Parameter | Units | Low | Medium | High
Household Size | Persons / Household | Census Tract Average | Census Tract Average | Census Tract Average
TN Loading to OSS | gm/person/day | 7 | 11.2 | 17
Denitrification | Percent | 40 | 25 | 10
Septic Tank Size | Liters | 3,407 | 3,407 | 3,407
TN in Septage | gm/L | 0.588 | 0.588 | 0.588
TN in Septic Tank When Pumped | gm | 2,003 | 2,003 | 2,003
Septic Tank Pumping Frequency | Years | 3 | 5 | 10

## Slide 8: ROSS – Data Output Summary
 | Units | TN Generated by 6,044 Households | Denitrification | Average Annual TN Removed by Pumping | Total N
LOW | Grams/Year | 54,636,835 | (10,927,367) | (4,035,377) | 39,674,091
 | Lbs/Year | 120,454 | (24,091) | (8,896) | 87,466
 | Tons/Year | 60.23 | (12.05) | (4.45) | 43.73
MEDIUM | Grams/Year | 87,418,937 | (13,112,840) | (2,421,226) | 71,884,870
 | Lbs/Year | 192,726 | (28,909) | (5,338) | 158,479
 | Tons/Year | 96.36 | (14.45) | (2.67) | 79.24
HIGH | Grams/Year | 132,689,457 | (13,268,946) | (1,210,613) | 118,209,898
 | Lbs/Year | 292,530 | (29,253) | (2,669) | 260,608
 | Tons/Year | 146.27 | (14.63) | (1.33) | 130.30

## Slide 9: Migrant Population Effect on ROSS
Ag Producers Supplement their workforce with migrant workers during peak periods
  ROSS calculations are for permanent residents only.
  A migrant worker is defined as a farm worker whose employment requires travel that prevented the worker from returning to his/her permanent place of residence the same day (USDA NASS 2014)
  In 2012 there were 9,598 migrant workers employed by agriculture throughout all of Yakima County (USDA NASS 2014).
  Prorating the number of migrant workers by crop acres county-wide results in a GWMA migrant worker population of 2,687 migrant workers (28% of county total)
  Annualized migrant population = 224 full time persons (assumed to reside in GWMA area)
  Adds low, medium, and high TN loading of 0.5, 0.9, and 1.4 tons per year

## Slide 10: ROSS Loading per Acre
Estimated area for all GWMA ROSS = 398 acres
  Based on NRCS soil type and corresponding DOH infiltration rate at each drainfield
  Based on a design flow of 60 gallons per person per day using household size at each drainfield
  Based on infiltration trenches 1’ wide, 60’ long, 5’ lateral separation
  Based on ROSS TN loading calcualtions
Results:
  Low – 223 pounds per acre
  Medium – 403 pounds per acre
  High – 662 pounds per acre

## Slide 11: LOSS Data
Two LOSS within GWMA Area
  Zillah LOSS – Large fruit packing operation and warehouse
    Operates 12 months per year
    Design capacity – 5,000 gallons per day
    TN Loading predominately human waste – TN loading = 8.7 gm/cap/day and water use = 16.2 gal/cap/day (EPA1992)
    WDOH design criteria results in capacity = 103 persons
    Results using ROSS methodology
      Low – 575 pounds per year (0.29 tons/year)
      Medium – 612 pounds per year (0.31 tons per year)
      High – 649 pounds per year (0.32 tons per year)

## Slide 12: LOSS Data (continued)
  Granger LOSS – Temporary Migrant Housing
    Operates 1month per year
    Design capacity – 4,850 gallons per day
    TN Loading assumed equivalent to ROSS loading
    WDOH design criteria results in capacity = 27 persons
    Results using ROSS methodology
      Low – 9.0 pounds per year
      Medium – 16.0 pounds per year
      High – 27.0 pounds per year

## Slide 13: LOSS Output Summary
 | Low | Medium | High
Loading (lb N/acre) | 195 | 209 | 225
Loading (kg N/hectare) | 218 | 235 | 252
Total loading (ton N/year) | 0.29 | 0.31 | 0.34
Total loading (kg N/year) | 265 | 285 | 307

## Slide 14: COSS Data
COSS – refers to septic systems used for employees working at Ag businesses that operate year-round and are not classified as LOSS by WDOH
  52 CAFOs classified by herd size (WSDA)
  Number of employees based on herd size using ratio of cows to employees (Reed 1994)
  Equates to 869 full time employees
  TN = 8.7 gm/cap/day and water usage = 16.2 gallons/cap/day
  TN Loading Using ROSS methodology
    Low – 2.43 tons per year
    Medium – 2.59 tons per year
    High – 2.74 tons per year

## Slide 15: Residential Lawn Fertilizer
“Green” areas (grass, trees, shrubs) representing areas where fertilizer may be applied were determined using GIS and infrared orthophotography
Using the green layer, four representative areas within the GWMA were examined to determine the percentages of land area that were green. Each of the areas were one square mile in size and the buildings and crop lands were subtracted from the green areas.
  Urban – within City of Sunnyside
  Suburban – Outside City of Sunnyside, but within Sunnyside Urban Growth Boundary
  Rural High Density – within Outlook
  Rural Low Density – within County with large parcels

## Slide 16: Residential Lawn Fertilizer (continued)
Assumes the use of a 20-0-8 fertilizer applied once each year
  equates to 23.3 pounds/acre of nitrogen per year
Assumes a high, medium, and low percentage of residents who fertilize to be 80, 50, and 20 % respectively
Assumes no nitrogen lost to plant uptake, denitrification, or volatization

## Slide 17: Residential Lawn Fertilizer (continued)
Representative Area | Application | Green Area per Parcel (acres) | Number of Parcels | Green Area in GWMA (acres)
Urban | All parcels located in incorporated cities | 0.09 | 7,180 | 646
Suburban | All parcels located in UGA outside of cities | 1.25 | 892 | 1115
Rural high density | All rural parcels <= 5 acres | 0.64 | 3,285 | 2102
Rural low density | All rural parcels > 5 acres | 0.73 | 709 | 518
Totals |  |  | 12,066 | 4,381

## Slide 18: Residential Lawn Fertilizer (continued)
 | Low | Medium | High
Loading (lb N/acre) | 4.7 | 11.7 | 18.6
Loading (kg N/hectare) | 5.2 | 13 | 20.9
Total loading (ton N/year) | 10.2 | 25.5 | 40.8
Total loading (kg N/year) | 9,260 | 23,152 | 37,043

## Slide 19: Small Scale Commercial and Hobby Farms -Data
Refers to residential land uses other than lawns that may contribute nitrogen to the GWMA area
Includes residential parcels < 10 acres in size that are not included in WSDA’s crop inventory
Lawn areas and building footprints were deducted
Fertilizer application rates based on RCIM Workgroup recommendations
Assumes a high, medium, and low percentage of residents who fertilize to be 80, 50, and 20 % respectively

## Slide 20: Small Scale Commercial and Hobby Farms –Data (continued)
Parcel Size Range of Small-Scale Farm (acres) | Number of Parcels | Total Parcel Area (acres) | Lawn Area (acres) | Building Allowance @ 2,000 sf/parcel (acres) | Effective Area (acres)
0 to 2.5 | 2335 | 2,481.5 | 1,804.1 | 107.2 | 570.2
2.51 to 5.0 | 311 | 1,075.6 | 223.0 | 14.3 | 838.4
5.1 to 10.0 | 110 | 776.1 | 83.3 | 5.1 | 687.7
Totals | 2756 | 4,333.2 | 2,110.4 | 126.5 | 2,096.3

## Slide 21: Small Scale Commercial and Hobby Farms –Data (continued)
Parcel Size of Small-Scale Farm (acres) | Nitrogen Fertilizer Application (lb/acre/yr) | Nitrogen Fertilizer Application (kg/hectare/year)
0 ≤ 2.5 | 14 | 15.7
2.51 ≤ 5.0 | 21 | 23.5
5.01 < 10.0 | 28 | 31.4

## Slide 22: Small Scale Commercial and Hobby Farms –Data (continued)
Parcel Size of Small-Scale Farm | Small-Scale Farm Effective Area (acres) | Application (lbs) | TN Low at 20% (tons) | TN Medium at 50% (tons) | High at 80% (tons)
0 ≤ 2.5 Acres | 570.2 | 14 | 0.80 | 2.00 | 3.19
2.51 Acres ≤ 5.0 Acres | 838.4 | 21 | 1.76 | 4.40 | 7.04
5.01 Acres ≤ 10.0 Acres | 687.7 | 28 | 1.93 | 4.81 | 7.70
Total (ton N/year) |  |  | 4.48 | 11.21 | 17.94
Total (kg N/year) |  |  | 4,068 | 10,171 | 16,273